## Slide 1: Relaxed Consistency models and software distributed memory
Computer Architecture
Textbook pp.79-83

## Slide 2: Revisit to Readers-Writers Problem
０
１
Writer： writes data then sets the synchronization flag
Reader：waits until flag is set
Writer
Reader
Write(D，Data)；
Write(X,1)；
D
X
Polling until(X==1)；
Notes: Let’s revisit to the readers-writers problem. For sending data from the writer to the reader, I said first the writer writes the data, then write 1 to the synchronization variable.

## Slide 3: Readers-Writers Problem
１
Reader： reads data from D when flag is set, then resets the flag
Writer
Reader
０
Writer：waits for the reset of the flag
Ｄ
X
Polling until(X==0)；
Polling until(X==1)；
data＝Read(D)；
Write(X，0)；
Notes: The reader reads the synchronization variable, and if it is 1, it reads the data from D. It seems to be correct. But is it true?

## Slide 4: But is it true?
In most machines, the order of read/write access from/to different address is not guaranteed.
The order is kept when each processor uses the sequential consistency or the total store ordering (TSO).
Notes: If the order of read/write access from/to different address is guaranteed, it is true. But, in most recent machines do not keep it. Exactly speaking if the sequential consistency or the total store ordering is guaranteed it the machine, it can be done.
Today, I would like to talk about the problem.

## Slide 5: Coherence vs. Consistency
Coherence and consistency are complementary：
Coherence defines the behavior of reads and writes to the same memory location, while
Consistency defines the behavior of reads and writes with respect to accesses to other memory location.
Hennessy & Patterson “Computer Architecture the 5th edition” pp.353
Notes: The words coherence and consistency are complement. That is coherence defines the behavior or reads and writes to the same memory location, while consistency is for other memory location. Today, I am going to treat only consistency, that is the case of two accesses are done to/from the different addresses.

## Slide 6: Sequential Consistency
Both L1 and L2 are never established.
Reads and writes are instantly reflected to the memory in order.
P1:A=0;
A=1;
L1: if(B==0) …
P2:B=0;
B=1;
L2: if(A==0) …
Notes: First of all, let me explain about the sequential consistency. In this diagram, if both L1 and L2 are never established, the sequential consistency is guaranteed. I means that reads and writes are instantly reflected to the memory in order.

## Slide 7: Sequential Consistency is not kept because of the delay.
Thus, sequential consistency requires immediate update of
shared memory or acknowledge messages.
P1:A=0;
A=1;
L1: if(B==0) …
P2:B=0;
B=1;
L2: if(A==0) …
Notes: If it takes any delay to the memory or any change of the reference order, these two sentences can work at the same time. OK. let’s examine the problem for the access order in a single processor first.

## Slide 8: Sequential Consistency
Write(A)
Read（Ｂ）
ＳＹＮＣ
Write(C)
Read(D)
ＳＹＮＣ
Write(E)
Write(F)
Notes: In the sequential consistency model, every access must be done in the order described in the program.

## Slide 9: Total Store Ordering
Read requests can be executed before pre-issued writes to other address in the write buffer.
R→R R→W W→W W→R
→ shows the order which must be kept.
Used in common processors.
From the era of IBM370
Notes: In order to enhance the performance of a single processor, read requests are often executed before pre-issued writes to other address in the write buffer. Here, this arrow mark shows the order which must be kept. This is used in common processors fromt the era of IBM370.

## Slide 10: Total Store Ordering
CPU
Cache
Read
Write
Write
Buffer
Read operation
should be done
earlier as possible.
→ For avoiding interlock
by the data dependency
When the address in the write buffer is the same as the reading address,
the data are directly read out from the write buffer.
Notes: In order to avoid the interlock caused by the data dependency, the read operation must be done early as possible. So, it can be done before write requests in the write buffer. Of course, if the address in the write buffer is the same as the reading address, the data are directly read out from the write buffer. Note that we are today considering the consistency problem, not the coherent problem.

## Slide 11: Total Store Ordering
Write(A)
Read（Ｂ）
ＳＹＮＣ
Read(C)
Write(D)
ＳＹＮＣ
Write(E)
Write(F)
Order which must be kept
Notes: The diagram shows the order which must be kept. The order between this write and read is not have to be kept in the total store ordering.

## Slide 12: Partial Store Ordering
The order of multiple writes are not kept.
R→R R→W W→W W→R
Synchronization is required to guarantee the finish of writes
Used in SPARC
Sometimes, it is called ‘Processor Ordering’.
Notes: When there are multiple memory modules which have different access time, it is difficult to keep the order of multiple writes. So, the partial store ordering relaxes the order between two write requests. In this model, finish of writes must be guaranteed with the synchronization operations. This ordering model was used for SPARC microprocessors, and sometimes called the processor ordering.

## Slide 13: Partial Store Ordering
Write(A)
Read（Ｂ）
ＳＹＮＣ
Read(C)
Write(D)
ＳＹＮＣ
Write(E)
Write(F)

## Slide 14: Partial Store Ordering
CPU
Cache
Read
Write
Write
Buffer
CPU
Cache
Read
Write
Write
Buffer
Network
Partial Store Ordering is a natural model for distributed memory
systems
Notes: As this diagram shows, two write operations are issued to the different memory modules. That is, it is natural for distributed memory systems.

## Slide 15: Quiz
Which order should be kept in the following access sequence when TSO and PSO are applied respectively.
Write A
Read B
Write C
Write D
Read E
Write F
Notes: OK. then here is a quiz.

## Slide 16: Weak Ordering
All orders of memory accesses are not guaranteed.
R→R R→W W→W W→R
All memory accesses are finished before a synchronization.
The next accesses are not started before the end of synchronization.
Used in PowerPC
Notes: If there are several different memory modules, even for a single processor, it is difficult to keep the order of memory request. So, it is natural to relax all orders of memory accesses. We only need to keep the order between synchronization operation. That is, all memory accesses are finished before a synchronization operation, and the next access must not be started before the end of synchronization. This ordering model was adopted in IBM PowerPC.

## Slide 17: Weak Ordering
Write(A)
Read（Ｂ）
ＳＹＮＣ
Read(C)
Write(D)
ＳＹＮＣ
Write(E)
Write(F)
Notes: This is the diagram of the weak ordering.

## Slide 18: Memory Consistency maintenance on CC-NUMA
Consistency between different home memory must be relaxed.
  The data and related synchronization variables must be allocated on the same home memory.
Let’s focus on a single home memory:
  For the synchronization operation, sequential consistency must be kept.
  For other operation, the acknowledge messages can be omitted.
Notes: For keeping the memory consistency for CC-NUMA, first of all, consistency between different home memory must be relaxed. The data and related synchronization variables must be allocated on the same home memory.

## Slide 19: Required Acknowledge messages
Node １
Node 2
Node ３
Node ０
Ｓ
Ｓ
Write request
Invalidation
Ａｃｋ
D
Ｓ
Ｗｒｉｔｅ
D
Ack
→ I
１
１
0
Acknowledge messages
are needed to keep the order
of data update.
They are needed for synchronization
Notes: As I introduced in the previous lesson, a lot of acknowledge messages are needed for invalidation, but since the writing data uses a relaxed consistency model, they are not needed. The home can reply just after sending invalidation messages.

## Slide 20: Implementation of Weak Consistency
Write requests are not needed to wait for acknowledge packets.
Reads can override packets in Write buffer.
The order of Writes are not needed to be kept.
The order of Reads are not needed to be kept.
Before synchronization, Memory fence operation is issued, and waits for finish of all accesses.
Notes: We need to provide the memory fence operation for implementing the synchronization. Once this operation is issued, no access for the memory is accepted. They must wait for the finish of the synchronization operation.

## Slide 21: For further performance improvement
Synchronization operation is divided into Acquire and Release.
The restriction is further relaxed by division of synchronization operation.
Release Consistency
Notes: For further performance improvement, the Stanford university proposed a further relaxed model for CC-NUMA machine. In this model, a synchronization operation is divided into Acquire and Release. Considering two types of synchronization operations, the restriction is further relaxed. This model is called a release consistency.

## Slide 22: Release Consistency
・Synchronization operation is divided into acquire(read) and release(write)
・All memory accesses following acquire（SA) are not executed
until SA is finished.
・All memory accesses must be executed before release（SR)
is finished.
・Synchronization operations must satisfy
sequential consistency (RCsc)
・Used in a lot of CC-NUMA machines （DASH,ORIGIN）
Notes: In this model, all memory accesses following acquire are not executed until the acquire is finished, and all memory accesses must be executed before release is finished. This is why it is called the release consistency model.

## Slide 23: Release Consistency
SA→W SA→R W→SA R→SA SR→W SR→R W→SR R→SR
The order of SA and SR must be kept.
Notes: This is the relationship between acquire, release and other accesses. Of course, the order between SA and SR must be kept.

## Slide 24: Release Consistency
Write(A)
Read（Ｂ）
ＳＹＮＣA
Write(C)
Read(D)
ＳＹＮＣR
Write(E)
Write(F)
Notes: This shows the order which must be kept between multiple accesses.

## Slide 25: Overlap of critical section with Release Consistency
acquire
release
Load/Store
Load/Store
Load/Store
Load/Store
acquire
release
Load/Store
Load/Store
acquire
release
Load/Store
Load/Store
acquire
release
Load/Store
Load/Store
Load/Store
Load/Store
・The overlapped execution
of critical sections is allowed.
Notes: This diagram shows the benefit of the release consistency. Two critical sections can be executed in the overlapped manner.

## Slide 26: Weak/Release consistency model vs. PSO/TSO + extension of speculative execution
Speculative execution
  The execution is cancelled when branch mis-prediction occurs or exceptions are requested.
  Most of recent high-end processor with dynamic scheduling provides the mechanism.
If there are unsynchronized accesses that actually cause a race, it is triggered.
The performance of PSO/TSO with speculative execution is comparable to that with weak/release consistency model.
Notes: Recently, most of high performance processors provide the speculative execution. This mechanism can be used instead of the release consistency model. That is, if there are unsynchronized that actually causes a race, the roll back is trigered. However, the detection is difficult and the rollback has a large overhead, so it is difficult to say which approach is better.

## Slide 27: Glossary 1
Consistency Model: Consistencyは一貫性のことで、Snoop Cacheの所で出てきたが、異なったアドレスに対して考える場合に使う言葉。一方、Coherenceは同じアドレスに対して考える場合に用いる。
Sequential Consistency model: 最も厳しいモデル、全アクセスの順序が保証される
Relaxed Consistency model:Sequential Consistecy modelが厳しいすぎるので、これを緩めたモデル
TSO(Total Store Ordering):書き込みの全順序を保証するモデル
PSO(Partial Store Ordering):書き込みの順序を同期、読み出しが出てくる場合のみ保証するモデル
Weak Consistency 弱い一貫性、同期のときのみ一貫性が保証される
Release Consistency 同期のリリース時にのみ一般性が保証される。Acquire（獲得）がロック、Release（解放）がアンロック
Synchronization, Critical Section：同期、際どい領域

## Slide 28: Software distributed shared memory (Virtual shared memory)
The virtual memory management mechanism is used for shared memory management
  IVY (U.of Irvine), TreadMark(Wisconsin U.)
The unit of management is a page (i.e. 4KB for example)
Single Writer Protocol vs. Multiple-Writer Protocol
Widely used in Simple NUMAs, NORAs or PC-clusters without hardware shared memory
Notes: In the next segment, I am going to talk about the software distributed shared memory. This mechanism is introduced for the machine without the cache coherent mechanism. The ideal is to use the virtual memory management mechanism for keeping the shared memory. So, the unit of management is a page, not a cache block.

## Slide 29: A simple example of software shared memory
Data Read
PC A
PC B
Shared Page
Page
Fault!
Home PC
Interrupt！
Notes: Let me explain a simple example of software shared memory. Assume three processors share software shared memory. When a PC A requests to read a shared page which is allocated on this home PC, it causes the page fault. Instead of getting the page from the disk, it sends the request to the home PC. When the request message is received, the home PC is interrupted and the software manager is invoked. It returned the requested page to the PC A.

## Slide 30: Representative Software DSMs
Name | University | SW/MW | Consistency model
IVY | Univ.Irvine | SW | Sequential
CVS | Univ. of Maryland | SW | Lazy release
TreadMarks | Washington Univ. | MW | Lazy release
Munin | Rice Univ. | MW | Eager release
Midway | CMU | MW | Entry
JIAJIA | Chinese Academy of Science | MW | Scope
Whether the copies are allowed for multiple writers
The timing to send the messages
Notes: This table shows the representative software distributed memory systems. It is classified into single writer and multiple writers. And the timing to send the messages.

## Slide 31: Extended relaxed consistency model
In CC-NUMA machines, further performance improvement is difficult by extended relaxed model.
Extended models are required for Software distributed memory.
  Eager Release Consistency
  Lazy Release Consistency
  Entry Release Consistency
Notes: In CC-NUMA machines, further performance improvement is difficult by extending the release consistency. However, for Software distributed memory, extended models are required. Thus, various types of extended consistency model has been proposed.

## Slide 32: Eager Release Consistency（１）
p1
p2
w(x)
w(y)
w(z)
rel
・In release consistency, write messages are sent immediately.
x
y
z
Notes: Eager Release Consistency is used in Munin. It reduces the number of message transfers. In release consistency, write messages are sent immediately.

## Slide 33: Eager Release Consistency（１）
p1
p2
w(x)
w(y)
w(z)
rel
x,y,z
・In eager release consistency, a merged message is
sent when the lock is released.
Notes: However, in eager release consistency, a merged message is sent when the lock is released.

## Slide 34: Single Writer Protocol
Data Write
PC A
PC B
Shared Page
Data Read
Request
Write back
request
Write back
Host PC
Only one writer is allowed
W
PC A W
PC A,B
Notes: This diagram shows the situation, in this case, only one writer is allowed.

## Slide 35: Eager Release Consistency（２）
・In Multiple-Writer Protocol, only difference is sent when released.
p1
p2
w(x)
w(y)
acq
acq
rel
rel
Page
updated y
updated x
updated x
diff
Notes: Eager release consistency can be extended to multiple write protocol. In this case, only difference is sent when released.

## Slide 36: Multiple Writers protocol
Write data
PC A
PC B
Twin
Shared Page
Twin memory is allocated when
target page is fetched.
Host PC
Notes: This diagram shows how the multiple writers protocol works. In this case, a twin memory is allocated when the target page is fetched.

## Slide 37: Multiple Writers protocol
PC A
PC B
Twin
Shared Page
Host PC
Notes: Multiple writers protocol allows for multiple PUs to write the same page at the same time.

## Slide 38: Multiple writers protocol
PC A
PC B
Twin
Shared page
Only difference
with twin is written back → Eager Release Consistency
Sync.
Write back
request
HOST PC
Notes: When write back is needed, the only difference with twin is written back.

## Slide 39: Lazy Release Consistency
p1
p2
p3
p4
acq r(x)
w(x) rel
acq w(x) rel
acq w(x) rel
・eager release consistency updates all copy pages.
Notes: The eager release consistency updates all copies pages when they are released.

## Slide 40: Lazy Release Consistency
p1
p2
p3
p4
w(x) rel
w(x) rel
w(x) rel
r(x)
・eager release consistency updates all copies.
・lazy release consistency only updates the page which
acquires the page.
acq
acq
acq
Notes: In order to reduce the number of messages, lazy release consistency only updates page which

## Slide 41: Entry Release Consistency（１）
Shared data and synchronization objects are associated
・It executes acquire or release on a synchronization object
→Only guarantees consistency of the target shared data
・By caching synchronization object, the speed of entering
a critical section is enhanced (Only for the same processor)
・Cache miss (Page fault) will be reduced by associating
synchronization object and corresponding shared data.
Notes: Entry release consistency fixes the combination of a shared data and associated synchronization object. The operation for keeping consistency is done only for the target data.

## Slide 42: Entry Release Consistency（２）
p1
p2
w(x)
acq S
rel S
・synchronization object S ⇔ shared data x,y
acq S
w(x)
r(y)
rel S
S, x,y
p3
・synchronization object R ⇔ shared data z
w(z)
acq R
rel R
w(z)
acq R
rel R
Notes: Assume that the synchronization object S is associated into the shared data x,y and synchronization object R is associated to the shared data z. The illustrated data exchange is only required.

## Slide 43: Summary
・Researches on relaxed consistency models are almost closing:
  Further relax is difficult.
  The impact on the performance becomes small.
  Speculative execution with PSO/TSO might be a better solution.
Software DSM approach is practical.
Notes: Let me explain today’s lesson.

## Slide 44: Glossary 2
Virtual Shared Memory: 仮想共有メモリ、仮想記憶機構を利用してページ単位でソフトウェアを用いて共有メモリを実現する方法。Single Writer Protocolは、従来のメモリの一貫性を取る方法と同じものを用いるが、Multiple Writers ProtocolはTwin(双子のコピー）を用いてDifference(差分）のみを送ることで効率化を図る。IVY,TreadMark,JiaJiaなどはこの分散共有メモリのシステム名である。
Eager Release consistency: Eagerは熱心な、積極的なという意味で、更新を一度に行うことから（だと思う）
Lazy Release consistency: Lazyはだらけた、という意味で、必要なところだけ更新を行うことから出ているが、Eagerに合わせたネーミングだと思う。
Entry Release consistency: Entry単位でconsistencyを維持することから出たネーミングだと思う。

## Slide 45: Exercise
Which order should be kept in the following access sequence when TSO,PSO and WO are applied respectively.
SYNC
Write
Write
Read
Read
SYNC
Read
Write
Write
SYNC

## Slide 46: How to use ITC machine
login to the assigned ITC Linux machine
  If you use windows 10, open command prompt
  ssh login_name@XXXX.educ.cc.keio.ac.jp
Get the compressed file:
  wget http://www.am.ics.keio.ac.jp/comparc/open20.tar
  tar xvf open20.tar
  cd open
https://keio.box.com/s/uwlczjfq4sp73xsni2c1y4vbwrk3ityp
Notes: Then, let’s use OpenMP. First, you should login ITC Linux machines and get the tar file.