## Slide 1: Synchronization with shared memory
AMANO, Hideharu
Textbook pp.60-68
Notes: We have learned the structure of shared memory. Now, let’s see the synchronization methods using the shared memory.

## Slide 2: Fork-join: Starting and finishing parallel processes
fork
Usually, these processes (threads)
can share variables
fork
join
join
Fork/Join is a way of synchronization
However, frequent fork/joins degrade performance
Operating Systems manage them
These processes communicate with
each other
Synchronization is required !
Notes: First of all, let’s check how we start the parallel processing with the shared memory. Usually, a single process starts, and when it executes fork operation to generate multiple processes. Some child-process can execute fork again. After executing in parallel, all processes execute join operation. At that time, processes except for only a process which executes the fork operation are terminated. When all processes are terminated with the join operation, the total program is finished. This join operation is a kind of synchronization. For example, OpenMP which I will explain in the later class uses this method. That is, parallel programming can be done only with fork-join mechanism. But, since they need heavy overhead, we need other method for synchronization.

## Slide 3: Synchronization
An independent process runs on each PU (Processing Unit) in a multiprocessor.
  When is the data updated?
    Data sending/receiving (readers-writers problems)
  A PU must be selected from multiple PUs.
    Mutual exclusion
  All PUs wait for each other
    Barrier synchronization
Synchronization
Notes: In MIMD processors, an independent process runs on each processing unit. In this case, a processing unit cannot recognize when the data are written into the shared memory from other processing units. Without the synchronization method, data sending/receiving cannot be done. This is called the readers-writers problem. In some cases, a processing unit must be selected from multiple Processing Units. This is called the mutual exclusion. In other cases, all PUs must wait for others. This type of synchronization is called a barrier synchronization.

## Slide 4: Readers-Writers Problem
０
１
Writer： writes data then sets the synchronization flag
Reader：waits until flag is set
Writer
Reader
Write(D，Data)；
Write(X,1)；
D
X
Polling until(X==1)；
Notes: Let me explain the readers-writers problem, first. Assume that a writer wants to send a data block to a reader. In such a case, a writer writes a data into a region in the shared memory. After that it changes the synchronization variable or synchronization flag X into 1. Note that this variable must be initialized to 0.

## Slide 5: Readers-Writers Problem
１
Reader： reads data from D when flag is set, then resets the flag
Writer
Reader
０
Writer：waits for the reset of the flag
Ｄ
X
Polling until(X==0)；
Polling until(X==1)；
data＝Read(D)；
Write(X，0)；
Notes: The reader reads X and if it is 0, it must check again. This operation is called poling or busy waiting. When the reader gets 1, it recognizes the sender has written the data. It reads the data block, then it resets the X into 0.

## Slide 6: Readers-Writers Problem
0
Reader： reads data from D when flag is set, then resets the flag
Writer
Reader
Writer：waits for reset of the flag
Ｄ
X
Polling until(X==0)；
Then write other data
Notes: The writer checks X and if X is 0, it can write the next data if needed.

## Slide 7: But is it true?
In most machines, the order of read/write access from/to different address is not guaranteed.
The order is kept when each processor uses the sequential consistency or the total store ordering (TSO).
→ This will be treated later.
Notes: This scenario is true if the order of read/write access from/to different address is guaranteed. Unfortunately, it is not guaranteed in some machines. I will introduce this subject in the next class, but when a processor uses the sequential consistency or the total store ordering (TSO), the scenario is established.

## Slide 8: Multiple Readers
０
３
Writer： writes data into D, then writes 3 into c.
Reader： Polling until( c!=0 )
(Each reader reads data once.)
Writer
Reader
D
c
Write(D，Data)；
Write(c，3)；
Notes: Then, what happens when multiple readers want to receive the data. The simple idea is replacing the synchronization flag X into a counter. When there are three readers, after the write writes the data, it writes a number of readers, three this case, into the counter c.

## Slide 9: Multiple Readers Iterative execution
３
Reader: decrements c
Writer：waits until c==0
Writer
Reader
３－１
２
２－１
１
There is a problem!!
Polling until(c==0)；
Polling until(c!=0)
data = Read(D);
counter = Read(c)；
Write(c，counter-1)；
Polling until(c==0);
１－１
０
Notes: The reader can recognize that the written data are available. So, after reading the data, it decrements the counter. When all readers finish to read, the counter becomes zero. The writer waits for the counter being zero, and then it writes the next data if needed. This operation seems to work well. But, there is a problem, since it introduces the mutual exclusion problem.

## Slide 10: The case of No Problem
３
３
３－１＝２
２
２
２
２－１＝１
counter=Read(c)；
Write(c，counter-1)；
counter=Read(c)；
Write(c，counter-1)；
１
１
Shared data
PU
An example of correct operation
１－１＝０
１
０
Notes: This slide shows the case without any problem. If the Processing Unit accesses the counter in order, it does not cause any problem.

## Slide 11: The Problematic Case
３
３
３－１＝２
２
３－１＝２
３
２
Multiple PUs may get the same number (2)
The value never changes to 0
An example of incorrect operation
Notes: However, what happens when multiple PUs tries to access the counter almost at the same time. When this PU gets three, during it decrements the value, the next PU can read data. It means that two PUs can get the same value 3. In this case, they both write two in the counter, and it never becomes to zero.

## Slide 12: Indivisible (atomic) operation
The counter is a competitive variable for multiple PUs
A write/read to/from such a competitive variable must be protected inside the critical section.
  A section which is executed by only one process.
For protection, an indivisible operation which executes continuous read/write operations is required.
Notes: The counter in this example, is called a competitive variable. To such a competitive variable, accesses must be done in the critical section. It means a section which is executed by only a process. This problem can be solved by introducing atomic or indivisible operation.

## Slide 13: An example of an atomic operation （Test and Set）
０
０
１
ｔ=Test&Set(X)
１
１
１
Reads x and if 0 then writes 1 indivisibly.
Polling until
(Test & Set(X)==0)；
ｃｒｉｔｉｃａｌ ｓｅｃｔｉｏｎ
Write（X，0）；
Notes: Let me explain the concept of an atomic operation with a simple example Test and Set. This operation reads a variable and writes 1 indivisibly if it is 0. The important point is that reading the data and writing 1 are executed with an action, that is, without interfering by other processors or processes. If multiple processors execute Test and Set to a variable, only one can get 0. It can execute the critical section. After doing it, it must release the critical section by writing 0. Then another processor can get 0 and enter the critical section.

## Slide 14: Various atomic operations
Swap(x,y): exchanges shared variable x with local variable y
Compare & Swap (x,b.y): compares shared variable x and constant b, and exchanges according to the result.
And-write/Or-write: reads bit-map on the shared memory and writes with bit operation.
Fetch & *(x,y): general indivisible operation
  Fetch & Dec(x): reads x and decrements (if x is 0 do nothing).
  Fetch&Add(x): reads x and adds y
  Fetch&Write1: Test & set
  Fetch&And/Or: And-write/Or-write
Most of them are used in RISC-V/A as atomic memory operations
Notes: Various atomic operations have been used, and most of them are used in RISC-V as atomic memory operations.

## Slide 15: An example using Fetch&Dec
３
Writer
Reader
３－１
２
２－１
１
Polling until(c==0)；
ｄａｔａ = Ｒｅａｄ（Ｄ）；
Ｆｅｔｃｈ＆Ｄｅｃ(c)；
Polling until(c==0)；
１－１
０
Notes: The convenient operation is Fetch&Dec. It reads the data and decrement it indivisibly. The counter can be directly the target of this operation. So, multiple readers problem can be easily solved without using the critical section. The fetch and decrement has two implementations, one is saturated and the other is non-saturated. In the case of saturated, it the reading value is zero, it is not decremented anymore.

## Slide 16: Load Reserved（Locked)/Store Conditional
Using a pair of instructions to make an atomic action.
lr （Load Reserved): Load Instruction with Lock.
sc (Store Conditional): If the contents of the memory location specified by the load reserved are changed before sc to the same address (or context switching occurs), it fails and returns 0. Otherwise, returns 1.
Atomic Exchange using lr/sc (x4<-> Memory indicated by x1)
try: mov x3,x4
lr x2,0(x1)
sc x3,0(x1)
beqz x3,try
mov x4,x2
RISC-V/A mainly uses them for synchronization.

## Slide 17: The benefit of lr/sc
Locking bus system is not needed.
Easy for implementation
  lr: saves the memory address in the link register
  sc: checks it before storing the data
  Invalidated with writing the data in the same address like the snoop cache.
Notes: This pair style of synchronization operations load reserved / store conditional has the following benefits.

## Slide 18: Implementing lr and sc
1000
lr x2,0(x1)
R1=0x1000
Link register
1000
lr x2,0(x1)
R1=0x1000
Memory
Data in 1000
is read out.
Cache is omitted in this diagram
PE1
PE2
Notes: When lr is executed, the address is set in the link register attached to each processing element.

## Slide 19: Implementing lr and sc
-
R1=0x1000
Link register
1000
sc x3,0(x1)
x1=0x1000
Memory
PE
Snoop and Invalidate
R3
PE1
PE2
PE2 executes sc first
‘1’ is returned to x3
Notes: When a PE executes store conditional, the link register is cleared if the address matches. If the link register is alive, it can get 1.

## Slide 20: Implementing lr and sc
-
R1=0x1000
Link register
-
sc x3,0(x1)
Memory
PE
Snoop and Invalidate
x3
PE1
PE2
Then, PE1 executes sc
‘0’ is returned to x3
X
The data is not written
Notes: When the other PE executes store conditional operation, it gets 0 since the link register is cleared.

## Slide 21: Quiz
Implement Fetch and Decrement by using lr and sc.
Notes: An atomic memory operations can be implanted with a combination of lr and sc.

## Slide 22: Answer
try: lr x2,0(x1)
addi x3,x2,#-1
sc x3,0(x1)
beqz x3,try
If sc is successful, the memory was decremented without interference.
Notes: This is an answer, if sc is successful, it means that the memory was decremented without interference.

## Slide 23: Multi-Writers/Readers Problem
Writer
Reader
２
１
Selects a writer from multiple writers
ｄａｔａ = Ｒｅａｄ（Ｄ）；
Ｆｅｔｃｈ＆Ｄｅｃ(c)；
Polling until(c==0)；
1 Writer-Multi Readers
Mutual exclusion
3
0
Notes: Once the critical section can be used, multi-writers problem can be easily solved. First, a writer is selected with a mutual exclusion operation by using Test and Set for example. Then, the writer executes the single-writer multiple readers problem.

## Slide 24: Glossary 1
Synchronization: 同期、今回のメインテーマ
Mutual exclusion: 排他制御、一つのプロセッサ(プロセス）のみを選び、他を排除する操作
Indivisible(atomic) operation: 不可分命令、命令実行中、他のプロセッサ(プロセス）が操作対象の変数にアクセスすることができない
Critical Section: 排他制御により一つのプロセッサ(プロセス）のみ実行することを保証する領域、土居先生はこれを「際どい領域」と訳したが、あまり一般的になってない
Fork/Join:フォーク／ジョイン
Barrier Synchronization: バリア同期
Readers-writers problem：そのまま呼ばれる。Producer-Consumer Problem（生産者、消費者問題）と類似しているがちょっと違う。

## Slide 25: Implementation of a synchronization operation
PU
PU
Snoop
Cache
PU
Snoop
Cache
PU
Snoop
Cache
Main Memory
A large bandwidth shared bus
1 (DE)
Test
&
Set
Read
0
Modify
Write
1
Bus mastership is locked
between Read/Write operation
0
Notes: Next, let me explain how the synchronization operations are implemented on the system with private or snoop cache. For example, when Test and Set is implemented on a multi-core system with snoop cache that I explained in the previous class, it will read the main memory and write it locking the bus. Apparently, the value becomes DE since this operation accompanies the write operation.

## Slide 26: Snoop Cache and Synchronization
PU
PU
PU
Snoop
Cache
PU
Snoop
Cache
Main Memory
A large bandwidth shared bus
1 (DE)
Test
&
Set
Test
&
Set
1(CS)
Even for the line with CS,
Test & Set requires
Bus transaction
0
→CS
Notes: If multiple PUs try busy waiting, bus will be congested because multiple PUs try to access the bus for the Test & Set operations.

## Slide 27: Test，Test＆Set
PU
PU
PU
Snoop
Cache
PU
Snoop
Cache
Main Memory
A large bandwidth shared bus
Test&Set
Test
Test does not require bus,
except the first trial
DE does not require bus transaction
Test&Set（c） if c == 0
0
1
Test
Polling
for CS
line
1
Notes: Just by reading the synchronization variable before executing the atomic operation, we can avoid this bus congestion. It is called test test & set. When reading data from the main memory is 1, it is hopeless to try the test and set. In this case, try just reading again.

## Slide 28: Test，Test＆Set
PU
PU
PU
Snoop
Cache
PU
Snoop
Cache
Main Memory
A large bandwidth shared bus
Cache line is invalidated
Release critical section
by writing 0
Test&Set（c） if c == 0
1
1
0
0
-
Invalidation
signal
Notes: After executing the critical section, a PU writes 0 to release the critical section. At that time, the invalidation signal is transferred on the bus, and other copies are invalidated.

## Slide 29: Test，Test＆Set
PU
PU
PU
Snoop
Cache
PU
Snoop
Cache
Main Memory
A large bandwidth shared bus
Release critical section
by writing 0
Test&Set（c） if c == 0
0
0
-
Write back
Test
Notes: When other PUs reads the synchronization variable. Since it was invalidated, it causes cache-miss, and the value 0 is transferred from the cache which released the critical section. Since the requesting PU gets 0, it executes Test&Set operation. Of course, there may be multiple PUs which get the value 0, but they can be resolved by executing Test&Set.

## Slide 30: Test，Test＆Set
PU
PU
PU
Snoop
Cache
PU
Snoop
Cache
Main Memory
A large bandwidth shared bus
Test & Set is really executed
Test&Set（c） if c == 0
0
Test & Set
If other PU issues the request, only a PU is selected.
0
-
Notes: As a result, only a PU can be selected.

## Slide 31: Lock with lr/sc
lockit: lr x2,0(x1) ; load reserved
bnez x2,lockit ; not-available spin
addi x2,x0,#1 ; locked value
sc x2,0(x1) ; store
beqz x2,lockit ; branch if store fails
Since the bus traffic is not caused by lr instruction, the same effect as test-test-and set can be achieved.
Notes: This code is a lock operation by using lr and sc. Since the bus traffic is not caused by lr instruction, the same effect as test-test-and-set can be achieved.

## Slide 32: Semaphore
High level synchronization mechanism in the operating system
A sender (or active process) executes V(s) (signal), while a receiver (or passive process) executes P(s) (wait).
P(s) waits for s = 1 and s ← 0 indivisibly.
V(s) waits for s = 0 and s ←1 indivisibly.
Busy waiting or blocking
Binary semaphore or counting semaphore
Notes: I have introduced basic synchronization mechanisms for multi-cores, but the synchronization operation is needed for operating system which handles concurrent processing of multiple processes. That is, concurrent processes must be treated as the same way of multiprocessors. However, since synchronization operations are implemented mainly with software, sophisticated mechanisms are used. Semaphore is famous synchronization mechanism.

## Slide 33: Monitor
High level synchronization mechanism used in operating systems.
A set of shared variables and operations to handle them.
Only a process can execute the operation to handle shared variables.
Synchronization is done by the Signal/Wait.
Notes: Monitor is also famous example of synchronization. For the safe operation, a set of shared variables and operations to handle them are defined.

## Slide 34: Synchronization memory
Memory provides tag or some synchronization mechanism
  Full/Empty ｂｉｔ
  Memory with Counters
  Ｉ-Ｓｔｒｕｃｔｕｒｅ
  Ｌｏｃｋ/Ｕｎｌｏｃｋ
Notes: Next, let me explain the synchronization memory. Instead of providing atomic operation, the synchronization mechanism can be provided on the memory.

## Slide 35: Ｆｕｌｌ／Ｅｍｐｔｙ Ｂｉｔ
０
Ｗｒｉｔｅ
→１
A data cannot read from 0
A data can write into 1
Suitable for 1-to-1 communication
１
Ｗｒｉｔｅ
Ｘ
１
Ｒｅａｄ
→０
０
Ｒｅａｄ
Ｘ
Notes: Full/Empty bit is the simplest one. There is a flag for each word of the memory.

## Slide 36: Memory with counters
０
Ｗｒｉｔｅ
→５
A data cannot read from 0
A data cannot write except 0
Suitable for 1-to-many communication
５
Ｗｒｉｔｅ
Ｘ
５
Ｒｅａｄ
→４
０
Ｒｅａｄ
Ｘ
A large memory is required for tag
Notes: Instead of providing the flag, we can provide the counter.

## Slide 37: Ｉ－Ｓｔｒｕｃｔｕｒｅ
PU
Snoop
Cache
PU
Snoop
Cache
PU
Snoop
Cache
PU
Snoop
Cache
Main Memory
A large bandwidth shared bus
Full/Empty with informing mechanism to the receiving PU
An example using
Write-update
Snoop cache
Interrupt
Notes: I-structure is a mechanism with informing system with the synchronization memory. This slide shows an example of implementing write-update style snoop cache. This idea was proposed for data flow machines.

## Slide 38: Ｌｏｃｋ/Ｕｎｌｏｃｋ
Ｐｒｏｃｅｓｓ
Ｌｏｃｋ
Ｐｒｏｃｅｓｓ
Ｌｏｃｋ
Ｐｒｏｃｅｓｓ
Ｌｏｃｋ
Ｐｒｏｃｅｓｓ
Ｌｏｃｋ
Ｐｒｏｃｅｓｓ
Ｌｏｃｋ
Ｐａｇｅ／block
Only registered processes can be written into the locked page.
Notes: Lock/unlock register can be provided for a certain block of the memory, for example, a page or block of the cache. When a process can write the page when lock bit is not set. At the first write, the lock bit is set and the process number is registered. Only the process whose id matches the register can write the block.

## Slide 39: Barrier Synchronization
Barrier；
Barrier；
Barrier；
Established
All processors (processes) must wait for the barrier establishment.
Wait for other processes
Barrier Operation： Indivisible operations like Fetch&Dec
Dedicated hardware
Notes: Barrier synchronization is a simple and easy to use. When a processor executes a barrier operation, it must wait other processors execute the barrier operation. When all processors execute the barrier operation, they can go forward. When multiple processors compute different part of a matrix with iteration, after writing results, they execute the barrier operation. When the barrier is established, all results are available, so they can go to the next iteration. Barrier operation can be implemented with atomic instructions, but since it is so popularly used, the special hardware is sometimes provided.

## Slide 40: Dedicated hardware
Open collecter
or
Open Drain
１
０
１
Reaches to the barrier
Not yet
Reaches to the barrier
If there is 0, the entire line becomes 0
Notes: This is an example of the simplest barrier implementation. Only a wire for the open drain output is enough. It is also useful for the debugging.

## Slide 41: Extended barrier synchronizations
Group barrier：A certain number of PUs form a group for a barrier synchronization.
Fuzzy barrier：Barrier is established not at a line, but a zone.
  Line barrier vs. Area barrier
Notes: Extended barrier synchronizations have been proposed.

## Slide 42: Fuzzy barrier
PREP；
PREP；
Establish
X
X
X
PREP;
Prepare (PREP) or Synchronize (X), then barrier is established.
Notes: This diagram explains the fuzzy barrier.

## Slide 43: Fuzzy barrier (An example)
Z[i]= s; PREP；
Z[j]=p; PREP；
Establish
Read Z
Read Z
Read Z
Z[k]=q; PREP;
Write the array Z → PREP
Read from Z → Synchronize (X)
PU0
PU1
PU2
PU3

## Slide 44: Summary
Synchronization is required not only for bus connected multiprocessor but for all MIMD parallel machines.
Consistency is only kept with synchronization →Consistency Model
Synchronization with message passing → Message passing model

## Slide 45: Glossary 2
Semaphore: セマフォ、腕木式信号機からでている。二進セマフォ（Binary Semaphore）とカウンティングセマフォ（Counting Semaphore)がある
Monitor: モニタ、この言葉にはいろいろな意味があるが、ここでは同期操作と変数を一体化して管理する手法、オブジェクト指向の元祖のひとつ
Lock/Unlock: ロック／アンロック、この辺の用語は、ほぼそのまま呼ばれる。
Fuzzy Barrier： ファジーバリア、バリアの成立時期に幅がある。

## Slide 46: Exercise
Write a program for sending a data from PU A to PU B,C,D only using Test & Set operations.