## Slide 1: Ｄｉｓｔｒｉｂｕｔｅｄ(Direct ) Interconnection Networks
AMANO, Hideharu
Textbook pp.１４０－１４７

## Slide 2: Ｄｉｓｔｒｉｂｕｔｅｄ（Direct Interconnection ）Networks
Nodes are connected with links directly.
Locality of communication can be used.
Extension to large size is easy.

## Slide 3: Basic direct networks
Linear
Ring
Central concentration
Tree
Complete connection
Mesh

## Slide 4: Metrics of Direct interconnection network（D and ｄ）
Diameter：D
  Number of hops between most distant two nodes through the minimal path
degree: d
  The largest number of links per a node.
D represents performance and ｄ represents cost
  Recent trends:
    Performance: Throughput
    Cost: The number of long links

## Slide 5: Diameter
２（ｎ－１）

## Slide 6: Other requirements
Uniformity：Every node/link has the same configuration.
Expandability: The size can be easily extended.
Fault Tolerance: A single fault on link or node does not cause a fatal damage on the total network.
Embeddability: Emulating other networks
Bisection Bandwidth

## Slide 7: bi-section bandwidth
The total amount of data
traffic between two halves of
the network.

## Slide 8: Hypercube
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111

## Slide 9: Routing on hypercube
0101→1100
Different bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111

## Slide 10: The diameter of hypercube
0101→1010
All bits are different
→ the largest distance
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111

## Slide 11: Characteristics of hypercube
D=d=ｌｏｇＮ
High throughput, Bisection Bandwidth
Enbeddability for various networks
Satisfies all fundamental characteristics of direct networks（Expandability is questionable）
Most of the first generation of NORA machines are hypercubes（iPSC，NCUBE，FPS-T）

## Slide 12: Problems of hypercube
Large number of links
  Large number of distant links
  High bandwidth links are difficult for a high performance processors.
Small D does not contribute performance because of innovation of packet transfer.
Programming is difficult: → Hypercube’s dilemma

## Slide 13: Is hypercube extendable?
Yes（Theoretical viewpoint）
  The throughput increases relational to the system size.
No（Practical viewpoint）
  The system size is limited by the link of node.

## Slide 14: Hypercube’s dilemma
Programming considering the topology is difficult unlike 2-D,3-D mesh/torus
Programming for random communication network cannot make the use of locality of communication.
2-D/3-D mesh/torus
  Killer applications fit to the topology
    Partial differential equation, Image processing,…
  Simple mapping stratedies
    Frequent communicating processes should be
    Assigned to neighboring nodes

## Slide 15: ｋ-ａｒｙ ｎ-ｃｕｂｅ
Generalized mesh/torus
K-ary n digits number is assigned into each node
For each dimension (digit), links are provided to nodes whose number are the same except the dimension in order.
Rap-around links (ｎ-1→０) form a torus, otherwise mesh.
“high-n” networks are used in recent supercomputers
  Tofu in K uses 6-torus
  Bluegene Q uses 5-torus

## Slide 16: k-ary n-cube
０
１
２
3-ary 1-cube
０
０
０
１
１
１
２
２
２
3-ary 2-cube
０
１
２
０
１
２

## Slide 17: k-ary n-cube
０
１
２
０
０
０
１
１
１
２
２
２
０
１
２
０
１
２
3-ary 1-cube
3-ary 2-cube
０
１
２
０
０
０
１
１
１
２
２
２
０
１
２
０
１
２
０
１
２
０
０
０
１
１
１
２
２
２
０
１
２
０
１
２
０
０
０
０
０
０
０
０
０
１
１
１
１
１
１
１
１
１
１
２
２
２
２
２
２
3-ａｒｙ 3-ｃｕｂｅ

## Slide 18: ３-ary 4-cube
0***
1***
2***

## Slide 19: ３-ary 5-cube
0****
1****
2****
degree: 2*n
Diameter: (k-1)*n

## Slide 20
6-dimensional Torus
Tofu

## Slide 21: Properties of k-ary n-cube
A class of networks which has Linear, Ring 2-D/3-D mesh/torus and Hypercube（binary n-cube） as its member.
Small d=2n but large D（O(k ))
Large number of neighboring links
k-ary n-cube has been a main stream of NORA networks. Recently, small-n large-k networks are trendy.
1/n

## Slide 22: Rise and fall of the members
k
n
10
2
100
1000
16
5
3
2
hypercube machines
1980’s
2D/3D Mesh/Torus 90’s-2000’s
5D/6D Mesh/Torus
2010’s
HW router
Wormhole, VC
Bandwidth requirement
Optical links,
Increasing size
Low-latency requirement

## Slide 23: Quiz
Calculate Diameter (D) and degree (d) of the６-ａｒｙ 4-cube (mesh-type).

## Slide 24: Glossary 1
Diameter:直径
degree:次数
Uniformity:均一性
Expandability:拡張性
Embeddability:埋め込み能力
Bisection bandwidth:2分割間転送量
Torus:両端が接続されたネットワークで、特にメッシュに対するものを指す。複数形はToriなので注意
ｎ-ary k-cube: n進ｋキューブ 2進キューブのことを特にハイパーキューブと呼ぶ

## Slide 25: Advanced direct networks
Shuffle based networks
  De Bruijn, Kautz, Pradhan
Extended mesh/torus
  Midimew, RDT
Star Graph
Hierarchical networks
  CCC, Hypernet
Circular networks
  Circular Omega、MDCE
Network inside the chip (Network-on-Chip)
  Spidergon, Mesh of Tree, Fat-H Tree
  Some of them might be classified into indirect networks

## Slide 26: De Bruijn network
000
001
010
100
101
011
111
110
0
1

## Slide 27: Routings for De Bruijn
000
001
010
100
101
011
111
110
0
1
Destination Routing
(001→101)

## Slide 28: B(k，n)
..
K-ary n-digits
..
0
..
1
..
k-1

## Slide 29: Characteristics of De Bruijn
Benefits
  d=2k、D=n=logN
  When k=2, d=4、D=logＮ，that is, d of 2-dimensional mesh but D of hypercube.
Problems
  Optimal routing is difficult (not established yet).
  Destination routing cannot make a best use of communication locality.
  No killer applications.
  Self loop and duplicated links

## Slide 30: Kautz network
010
101
210
102
020
202
021
212
121
012
120
201
The same number
should not be at the
neighboring digit

## Slide 31: Circular networks
Circular Omega
  Advantageous for one-way communication
  Used in data-flow machine EM-4
MDCE(CCCB)
  Hierarchical structure of Circular Omega（Banyan）
  Used in massively parallel machine RWC-1

## Slide 32: Circular Omega network
000
001
010
011
100
101
110
111
000
001
010
011
100
101
110
111

## Slide 33: Cube Connected Circular Banyan
Circular Banyan
3-Dimensional
Proposed for RWC-1

## Slide 34: Star graph
ABCD
BACD
BCDA
CBAD
CDAB
DCAB
CADB
DACB
ADCB
DBCA
BACD
CABD
DCBA
BDCA
CDBA
BDAC
ADBC
DABC
BADC
ABDC
DBAC
ACBD
CBDA
ACDB
Connection n! nodes

## Slide 35: Routing on Star graph
ABCD
BACD
BCDA
CBAD
CDAB
DCAB
CADB
DACB
ADCB
DBCA
BACD
CABD
DCBA
BDCA
CDBA
BDAC
ADBC
DABC
BADC
ABDC
DBAC
ACBD
CBDA
ACDB
ＡＢＣＤ → ＤＡＢＣ
３（ｎ－１）／２
If Ａ is top, change with arbitrary symbol,
else, change with the symbol of destination
node

## Slide 36: Hierarchical network
CCC(Cube Connected Cycles)
  ｈｙｐｅｒｃｕｂｅ＋loop
Hypernet
  Compete connection＋hypercube
Well combined, weak points of original networks are vanished.
Complicated routing, gap between hierarchies

## Slide 37: CCC(Cube Connected Cycles)
000
001
010
011
100
101
110
111
0
1
2

## Slide 38: Hyper Net
a
b
c
d
e
f
g
c
b
e
d
i
j
f
k
g
l
a
h
m
n
h
p
o
Other links are used for
further upper hierarchy

## Slide 39: Extended mesh/torus
Including mesh/torus structure
Extended links for performance enhancement
  Reconfigurable Mesh
  Midimew
  RDT

## Slide 40: RDT(Recursive Diagonal Torus)

## Slide 41: Multicasting on the RDT

## Slide 42: Topology for NoC: (1)
router
core
Spidergon
  Ring + diagonal links
  Node degree 3;
[Bononi, DATE’06]
[Coppola, ISSOC’04]
Spidergon (2-D layout)

## Slide 43: Topology for NoC: (2)
Mesh-of-Tree
WK-recursive (4,2)
router
計算コア
WK-recursive (d,k)
  hierarchical network
Mesh-of-Tree
  Mesh + Tree
[Vecchia, FCGS’88]
[Leighton, Math System theory’84]
[Rahmati, ICCD’06]

## Slide 44
router, Core
router, Core
(※) routers for more than rank-2 are omitted
Each core connects to Red tree and Black tree
Torus is formed
Fat H-Tree： A network topology for NoCs

## Slide 45: Glossary 2
De Bruijin:人の名前でドブロイアンと読むのが本来の読み方だが英語圏の人はこれをデブルージンと読むので注意（最初全然わかんなかった）

## Slide 46: Summary
Recently, practical new topologies are not proposed.
A lot of “made-in-Japan” networks
Asymmetric indirect networks will be widely used.

## Slide 47: Exercise
Compute diameter of CCC with 16 cycles each of which has 4 nodes.
Hint: How is the method to move between cycles efficiently?